## Slide 1: Salt 101

## Slide 2: Agenda
How salt works
How salt impacts the environment
MnDOT’s Salt Sustainability Initiative and MDSS

## Slide 3
“Snow and ice removal operations is one of the most critical functions of state and local transportation agencies in cold regions.”
Clear Roads

## Slide 4: Salt Institute
Plowing and salting can reduce injury crashes by up to 88%
A one day major snowstorm that shuts down roads can cost between $300 and $700 million
Deicing pays for itself within the first 25 minutes after salt is applied

## Slide 5: Salt is the most common deicer

## Slide 6: Two separate studies found that salt is the most cost effective deicer
Real Performance Characteristics of Deicing Salts Scott Koefod, Principal Scientist, Cargill Salt Group
Salt Brine Blending to Optimize Deicing and Anti-Icing Performance
Dr. Stephen Druschel, Principal Investigator,
Minnesota State University, Mankato
Notes: In their studies, both Scott Koefod and Stephen Druschel, determined that salt is the most cost effective deicer available.

## Slide 7: How does salt work

## Slide 8
Dry salt won’t break apart ice crystals
Salt only works when it is dissolved - It disassociates (separates into sodium and chloride ions)

## Slide 9: Salt
The sodium and chloride ions can then attach to the hydrogens and oxygens in the ice, to destroy the ice crystals
H+
H+
H+
O-
O-
N+
Cl-
H+

## Slide 10
As the temperature drops, the ability of the sodium and chloride ions to break apart ice crystals diminishes rapidly

## Slide 11
Speed of Melting is very temperature dependent
Notes: 11

## Slide 12: Dilution
Salt is most effective at a 23.3% solution
When melting occurs, the solution on the roadway becomes diluted

## Slide 13: Dilution
To minimize the dilution, snow must be plowed off the road before applying salt

## Slide 14: How sodium and chloride affect the environment

## Slide 15: Sodium
The sodium ion primarily causes problems in roadside soils
Excess amounts of sodium can adversely impact soil structure, making plant growth difficult

## Slide 16: Sodium
Reduces oxygen availability in the root zone
Restricts root growth and seed emergence
Increases erosion
Creates an environment where invasive species can thrive

## Slide 17: Chloride
The reason salt is so effective is also the reason it’s harmful to the water
The bond between the chloride and the hydrogen ions is not easily broken
H+
H+
H+
O-
O-
N+
Cl-
H+

## Slide 18: Chlorides in water
Chlorides do not break down, they stay attached to the water molecules
There is no practical way to remove chloride from water
The chloride continues to accumulate

## Slide 19: Minnesota Waters
MPCA 2016 Draft list of chloride impaired waters
47 water bodies listed for chloride

## Slide 20: Impaired means a pollutant exceeds the federal standard

## Slide 21: Chronic Standard for Chloride
230 mg/L
~ 1 teaspoon salt in 5 gallons of water

## Slide 22: Chronic conditions
Over time organisms don’t thrive, may die young, limited reproduction
Photo by J. W. Stewart

## Slide 23: Acute standard
860 mg/L
About 1 tablespoon salt in 5 gallons

## Slide 24
It is estimated that 350,000 tons of salt is used in Metro area every winter
(Number based on salt purchased)
Novotny, Sander, Mohseni and Stefan, 2008

## Slide 25
~70% of the chloride applied in the Metro area is unaccounted for
~30% of the chloride is leaving via the Mississippi River
Novotny, Sander, Mohseni, and Stefan 2008

## Slide 26: Chloride in lakes
Chloride can affect the spring and fall turnover of lakes
Turnover is important, it brings oxygen to the bottom of the lake
Mixed water
Heavy with chloride
Won’t mix

## Slide 27: Chloride in groundwater
A USGS study showed high levels of chloride in Metro groundwater
Groundwater supplies 75% of Minnesota’s drinking water
Photo: MN DNR

## Slide 28: Outside the Metro Area
Chloride concerns aren’t restricted the Twin Cities Metro Area
Tischer Creek in Duluth experiences spikes in chloride during spring melt

## Slide 29
MnDOT’s Salt Sustainability Initiative

## Slide 30: MnDOT Salt Sustainability Plan
Target: Within 5 years salt usage will be less than 10% above MDSS recommendations
Focus on 4-R’s
  Right material
  Right amount
  Right place
  Right time
Training
Post-storm meetings
Calibration
New technology/materials